## Slide 1
Digital Image Processing
Image Enhancement
Lecture # 4
1st Semester
2019-2020
Dr. Abdulhussein Mohsin Abdullah
Computer Science Dept., CS & IT College, Basrah Univ.

## Slide 2
The principal objective of enhancement is to process an images so that the result is more suitable than the original image for a SPECIFIC application
Category of image enhancement
  Spatial domain
  Frequency domain
Objective

## Slide 3: Image Transform
Image transforms can be simple arithmetic operations on images or complex mathematical operations which convert image from one representation to another.
Or
A function or operator that takes an image as its input and produces an image as its output. Depending on the transform , the input and output images may appear entirely differently and have different interpretations

## Slide 4: Need of Image Transforms:
Viewing an image in different domains enables the identification of features that may not be as easily detected in spatial domain.
Image transforms are used majorly in feature extraction, image compression and image enhancement.

## Slide 5
Spatial domain
  •The image plane itself
  •Processing in the spatial domain deals with direct manipulation of the image pixels
•Other domains
  •Frequency domain
    •Consider the image as a 2D signal and apply Fourier transform
    •Process the image in the transformed domain
    •Apply the inverse transform to return into the spatial domain.
Definitions

## Slide 6
•Types of transformations that can be applied to an image
  •Intensity transformations
    •Operate on single pixels
  •Spatial filtering (next lecture)
    •Working on a neighborhood of every pixel

## Slide 7: Basics
• Intensity transformation and spatial filtering
  • f : input image
  • g: output image
  • T: an operator applied to the image f
• In the discrete case
  • f and g are 2D matrices of size WxH
  • T is a matrix of size wxh which is much smaller than WxH
  • The value of each pixel of g is the result of applying the operator T at the corresponding location in f.
  • If wxh = 1x1  intensity transform
  • Otherwise, it’s spatial filtering.
3 x3 Nbd
y
(x,y)
x
Image f(x, y)
g(x, y) = T [f(x, y)]
Spatial Domain

## Slide 8: Basic intensity transforms
•Definition
•Examples
  •Image negatives
  •Log transformations
  •Power-law (Gamma) transformations
•In the following
  Each image is represented with a 2D matrix of L intensity levels. That is each pixel takes a value between 0 and L-1
g(x, y) = T [f(x, y)]

## Slide 9
1. Contrast stretching: (Normalization)
If T(r) has the form as shown in figure, the effect of applying the transformation to every
pixel of f to generate the corresponding pixels in g would:
  Produce higher contrast than the original by:
  Darkening the levels below k in the original image.
  Brightening the levels above k in the original image.
Contrast stretching: simple image enhancement technique that improves the contrast in an image by 'stretching' the range of intensity values it contains to span a desired range of
values; typically, it uses a linear scaling function
2. Thresholding:
  Produce a two-level (binary) image, a mapping of this form called thresholding function.
Intensity transformation example:

## Slide 10
Some basic grey-level transformation functions used for contrast enhancement
L=2k
k: number of bits used to represent each pixel
Basic transformation functions for contrast enhancement

## Slide 11
Image Negatives
s= (L-1)-r
s is the pixel value of the output image and r is the pixel value of the input image.
(left) Original digital mammogram. (right) Negative image obtained using the negative transformation
The negative transformation can be used to enhance white or gray
detail embedded in dark regions of an image.

## Slide 12
Logarithmic Transformations
s= c log(1+r)
s is the pixel value of the output image and r is the pixel value of the input image.
(left) Fourier spectrum of Barbara’s image.
(right) Result of applying the log transformation

## Slide 13
Log transformations
  –Maps a narrow range of low intensity values into a wider range of output values (spreading)
  –The opposite is true for the higher values of input levels (compressing)

## Slide 14
Power-law (Gamma) transformations
c and  are positive constants.
s = cr
The curves generated with values of g > 1 have exactly the opposite effect as those generated with values of g < 1 .

## Slide 15
Power-Law Transformations
c=1
 = 0.4
c=1
 = 0.3
c=1
 = 0.6

## Slide 16
Power-Law Transformations
c=1
 = 3
c=1
 = 5
c=1
 = 4

## Slide 17
Advantage
  Arbitrarily complex
Disadvantage
  More user input
Type of Transformations
  Contrast stretching
  Gray-level slicing
  Bit-plane slicing
Piecewise-Linear Transformation Functions

## Slide 18
Contrast Enhancement
Contrast Stretching: improves the contrast in an image by stretching the range of intensity values to span a desired range of values.
Contrast-stretching transformation is a process that expands the range of intensity levels in an image so that it spans the full intensity range of the recording medium or display device.

## Slide 19
Converts to black & white
s = T(r)
Intensity of g
Intensity of f
Linear Part contributes to the contrast stretching
Thresholding
Contrast
stretching
Transformation

## Slide 20
Contrast stretching
Low contrast images can result from poor illumination
Low contrast image

## Slide 21
Contrast Stretching
Objective: Increase the dynamic range of the gray levels in the image
Causes for poor image
  -Poor illumination
  -Wrong lens aperture
  -Wrong shutter speed
  -Lack of dynamic range in the imaging sensor

## Slide 22
The process of highlighting a specific range of intensities in an image often called intensity-level slicing,
Piecewise-Linear Transformations

## Slide 23: Gray-level Slicing
This technique is used to highlight a specific range of gray levels in a given image. It can be implemented in several ways, but the two basic themes are:
  One approach is to display a high value for all gray levels in the range of interest and a low value for all other gray levels. This transformation, shown in Fig 3.11 (a), produces a binary image.
  The second approach, based on the transformation shown in Fig 3.11 (b), brightens the desired range of gray levels but preserves gray levels unchanged.
  Fig 3.11 (c) shows a gray scale image, and fig 3.11 (d) shows the result of using the transformation in Fig 3.11 (a).

## Slide 24
Piecewise-Linear Transformations
grey-level slicing
Other pixel values are preserved
Pixel values between [A,B] are highlighted
Other pixel values are darkened

## Slide 25: Bit-plane Slicing
Pixels are digital numbers, each one composed of bits. Instead of highlighting gray-level range, we could highlight the contribution made by each bit.
This method is useful and used in image compression.
Most significant bits contain the majority of visually significant data.

## Slide 26
Since the given image has a maximum grey level of 7, it is a 3-bit image. We convert the image to binary and separate the bit planes.
Separating the bit planes, we obtain
2. Center bit plane
3 LSB Plane
1. MB Plane

## Slide 27
The three main goals of bit plane slicing is:
  Converting a gray level image to a binary image.
  Representing an image with fewer bits and corresponding the image to a smaller size
  Enhancing the image by focusing.

## Slide 28
Bit-Plane Slicing

## Slide 29
Bit-Plane Slicing

## Slide 30
Histogram Processing
Histogram : is the discrete function h(rk)=nk , where rk is the kth gray level in the range of [0, L-1] and nk is the number of pixels having gray level rk.
Normalized histogram : is p(rk)=nk/n, for k=0,1,…,L-1 and p(rk) can be considered to give an estimate of the probability of occurrence of ray level rk.

## Slide 31
for each gray level, count the number of pixels having that level
for each level, a stick represent the number of pixels (can group nearby levels to form a bin and count number of pixels in it)

## Slide 32
Size : 256 × 256 pixels,
8-bit pixel coding
Distribution of gray levels
in image [0 ; 255]

## Slide 33
•Consider the following 5x5 image

## Slide 34
8 × 8 Grayscale
image « A »
Matrix of gray levels of
image « A »
Histogram of
image « A »
Image « A » has 3 different gray levels : 0, 1 and 2.
Count the number of pixels for each gray level.
There are respectively 24, 12 and 28 pixels for the levels 0, 1 and 2
⇒ Histogram of image “A”

## Slide 35
Example
Let us read the grayscale image FRUIT_LUMI.BMP with the command imread. We can thus build the histograms for these grayscale images:
  I = imread(‘FRUIT_LUMI.BMP’) ;
  J = imread(‘ISABE_LUMI.BMP’) ;
  imhist(I);
  imhist(J);
The two peaks of pixel populations in the FRUIT_LUMI image histogram
correspond to the darkest image zones (ground, grape, etc.) and to the
zones which have a middle gray level (intensity close to 127 for apples,
background, etc.).

## Slide 36
function Normalized_Hist = Img_Hist(img)
[R,C]=size(img);
Hist=zeros(256,1);
for r = 1:R
for c=1:C
Hist(img(r,c)+1,1)=Hist(img(r,c)+1,1)+1;
end
end
Normalized_Hist = Hist/(R*C);
plot(Normalized_Hist)
Histogram Extraction using Matlab

## Slide 37
The normalized histogram function is the histogram function divided by the total number of the pixels of the image.
Normalized histogram
where n is the number of pixels in the image, and r is an intensity level.
–It is the frequency of appearance of each intensity level (color) in the image.
–It gives a measure of how likely is for a pixel to have a certain intensity.
That is, it gives the probability of occurrence the intensity.
–The sum of the normalized histogram function over the range of all intensities is 1.

## Slide 38
Image « A »
Intensity values of « A »
Cumulated histogram of
Cumulative Distribution Function (CDF)
If h is the normalized histogram of an image, the CDF of his define as:

## Slide 39
compute a special histogram thanks to the cumulative sum of histogram elements ⇒ cumulated histogram.
for each gray level “L”, the stick represents the cumulative sum of pixel number for all the gray levels lower or equal than L: levels 0, 1, and 2 are thus represented by 24, 36 and 64 pixels.
the cumulated histogram is useful to a lot of image processing such as highlight
for each gray level “L”, the stick represents the cumulative sum of pixel number for all the gray levels.

## Slide 41
•Goal
  Increase the global contrast of an image by design a transformation (mapping) T that that makes pixel intensities uniformly distributed over the whole range [0, L-1]
•Input
  •An image f of intensity levels in [0, L-1]
  •Intensity levels can be viewed as random variables
  •Let’s hf be the normalized histogram of f. hf is also the probability distribution function which we denote by Pf
  •r denoted intensity values of f
•Output
  •An image g= T(f) such that the intensities of g are uniformly over the range [0, L-1].
    •This will improve the contrast by spreading out the most frequent intensity values.
  •We denote by s = T(r).
Histogram equalization

## Slide 42
Histogram equalization is used to enhance image contrast and gray-level detail by spreading the histogram of the original image.
s = T ( r ) 0 r  1,
where r and s are normalized pixel intensities
Conditions for the transformation
T( r ) is single-valued and monotonically increasing in the
interval 0  r  1
(b) 0  T ( r )  1 for 0  r  1
1
Histogram Equalization

## Slide 43
Uniform probability distribution
  •A probability distribution P is uniform if all events have the same probability of occurrence.
  •If N is the number of events then P(x) = 1 / N for every event x.

## Slide 44
Histogram equalization
•We want to compute
  •An image g= T(f) such that the intensities of g are better distributed on the histogram hg
  •hg as a PDF, the intensities of g should follow a uniform distribution.

## Slide 45
•Requirements for a good mapping T
  •Condition A:T is required to be a monotonically increasing function in the interval [0, L-1]
    •That is if x < y T(x) <= T(y)
    •Avoids reversing intensities
  •Condition B:x  [0, L-1] T(x) [0, L-1]
    •This guarantees that the range of output intensities are the same as the range of input intensities.
  •Condition C:You may require strict monotonicity
    •x < y T(x) < T(y)
    •This guarantees the mapping (or transformation )T is one-to-one.

## Slide 46
Histogram equalization –Algorithm
•Input
  •A discrete image f of L levels of intensity
•Algorithm
  •Step1:Compute the normalized histogram hf of input image f
  •Step 2:Compute the CDF of hf, denoted CDFhf
  •Step 3:Find a transformation T: [0, L-1] [0, L-1] such that
  •Step 4: Apply the transformation on each pixel of the input image f
•Properties
  •The procedure is fully automatic and very fast
  •Suitable for real-time applications

## Slide 47
Example
  Do histogram equalization on the 5x5 image with integer intensities in the range between one and eight.

## Slide 49
Example

## Slide 50
Histogram equalization of color images
•For color images
  •Apply separately the procedure to each of the three channels
    •will yield in a dramatic change in the color balance
    •NOT RECOMMENED unless you have a good reason for doing that.
  •Recommended method
    •Convert the image into another color space such as the Lab color space OR HSL/HSV color space
    •Apply the histogram equalization on the Luminance channel
    •Convert back into the RGB color space.

## Slide 51
Lab color space
•Lab color space is designed to approximate the human vision
  •The L component matches the human perception of lightness
  •The Lab space is much larger than the gamut of computer displays.
•Conversions
  •Will be covered in a special lecture on Colors.

## Slide 52
Histogram Equalization
Histogram Equalization
Histogram of 4 basic grey-level characteristics

## Slide 53
Histogram of 4 basic grey-level characteristics
Low contrast image
High contrast image

## Slide 54
Histogram Processing

## Slide 55
Histogram matching
•Goal
  •Given an image f with a normalized histogram hf
  •Given a probability distribution P
  •Find a transformation T such that the normalized histogram of T(f) matches the probability distribution P.
•Remarks
  •If P is a uniform distribution then T is the same as the histogram equalization.

## Slide 56
Histogram matching -procedure
•Input
  •A source image f and a target distribution function P
  •P can be the normalized histogram of another image g
•Procedure
  •Calculate the histogram hfof f
  •Calculate the CDFf of f and the CDFP of P
  •For each gray level x[0, L-1], find the gray level y for which
    •CDFf(x) = CDFP(y)
    •We denote this mapping by M
    •Can be implemented as a lookup table
  •Apply the mapping M to all pixels of the input image f

## Slide 57
Is histogram equalization a good approach to enhance the below image?
Histogram Matching

## Slide 58
Histogram Matching method generates a processed image that has a specified histogram.
Input image
pr(r)
T (r)
s
Desired
Output image
pz(z)
G (z)
v
s  v, since both will have
approximately uniform pdf
z = G-1[T( s )]
s = G[T( r )]
Histogram Matching

## Slide 59
Histogram Matching

## Slide 60
1) Modify the histogram of
the image to obtain pz(z).
2) Find the transformation
function G (z) using the
modified histogram in
step 1.
3) Find the inverse G-1 (z)
4) Enhanced image is
obtained by applying G-1 to the
pixels of the histogram-equalized
image shown in Fig. 3.21.c
1 G (z)
2 G-1 (z)
Histogram Matching

## Slide 61
125
128
0.98
0.002
250
255
0.7
0.3
178
255
Local Histogram
Global Histogram
125
128
Local Histogram Enhancement

## Slide 62
Local Histogram Enhancement

## Slide 63
Contrast manipulation using local statistics, such as the mean and
variance, is useful for images where part of the image is acceptable,
but other parts may contain hidden features of interest.
Histogram Statistics for Image Enhanc.

## Slide 64
Let (x,y) be the coordinates of a pixel in an image, and let Sxy
denote a neighborhood (sub-image) of specified size, centered at
(x,y).
The local mean and variance are the decision factors to whether apply
local enhancement or not.
Histogram Statistics for Image Enhanc.

## Slide 65
MG: Global mean
DG: Global standard
deviation
E, k0, k1, k2: Specified parameters
E = 4,
k0 = 0.4,
k1= 0.02,
k2 = 0.4
Size of local area = 3  3
Histogram Statistics for Image Enhanc.

## Slide 66
125 135 145 135 ..
168 175 158 149 ..
210 231 215 129 ..
187 192 145 200 ..
174
Image
Mean
164
187
(x,y)
(x,y)
E
Histogram Statistics for Image Enhanc.

## Slide 67
Enhanced Image
Original Image
Histogram Statistics for Image Enhanc.

## Slide 68
Arithmetic/logic operations involving images are performed on a pixel-by-pixel basis between two or more images.
Arithmetic Operations
Addition, Subtraction, Multiplication, and Division
Logic Operations
AND, OR, NOT
Enhancement Using Arithmetic/Logic Op.

## Slide 69
AND
OR
Logic operations are performed on the binary representation of the pixel intensities
Enhancement Using AND and OR Logic Op.

## Slide 70
Enhancement Using Arithmetic Op. _ SUB
Original
4
Upper-order
Bit
Error
HE of
Error

## Slide 71
Problem:
The pixel intensities in the difference image can range from -255 to 255.
Solutions:
1) Add 255 to every pixel and then divide by 2.
2) Add the minimum value of the pixel intensity in the difference image
to every pixel and then divide by 255/Max. Max is the maximum
pixel value in the modified difference image.
Enhancement Using Arithmetic Op. _ SUB Mask Mode Radiography

## Slide 72
Original image
Noise with zero mean
Enhancement Using Arithmetic Op. Averaging

## Slide 73
Gaussian Noise
mean = 0
variance = 64
K = 8
K = 32
K = 16
K = 128
f(x,y)
g(x,y)

+
-
x
Enhancement Using Arithmetic Op. Averaging

## Slide 74
Difference images between original image and images obtained from averaging.
K = 8
K = 16
K = 32
K = 128
Notice the mean and variance
of the difference images
decrease as K increases.
Enhancement Using Arithmetic Op. Averaging