## Slide 1: Use and Care of the Microscope
Dr.
Zainab A. Hasan
2017

## Slide 2: Microscope is the device for magnifying objects that are too small to be seen with the naked eye. Magnification is the process of enlarging the size of an object , as an optical image

## Slide 3: Microscopes are divided into two categories : 1- Electron microscopes 2- Light microscopes

## Slide 4: 1- Electron microscopes : are subdivided into A- Scanning electron microscope (SEM) : In this microscope the electrons are used as the source of illumination instead of light . This microscope can have a magnification up to 100,000 X and it used to provide a three –dimensional view of cells.

## Slide 5: B- Transmission electron microscope (TEM): Also the electrons are used as the source of illumination and have a magnification of 100,000 X or greater , but it used to view very thin sections of cells to reveal their internal structure , and also used to study viral-infected cells .

## Slide 6: 2- Light microscopes : are subdivided into a- Fluorescent microscope : b- Bright –field microscope :

## Slide 7: a- Fluorescent microscope : The magnification of this microscope is 2600 X and its focuses ultraviolet light on a specimen , causing of some molecules in the specimen to be fluoresce .

## Slide 8: b- Bright –field microscope : This microscope is used to study the size , shape ,and arrangement of the microbial cells , but it provides little information about the internal cell structure . There is two types of this microscope : Simple microscope : It has a single lens magnifier. Compound microscope : It employs two or more lenses called ocular and objective lenses - Ocular lenses (10X) Monocular microscope ( Has one ocular lens) binocular microscope ( Has two ocular lens )

## Slide 9: - Objective lenses Scanning lens (4X) Low power lens (10X) High power lens (40X) Oil immersion lens(100X)

## Slide 10: The magnification of the microscope depends on the type of objective lens used with the ocular lens . So , the total magnification is calculated by multiplying the objective lens by ocular lens.
Total magnification |  | Ocular lens | Objective lens | 
40x | = | 10x | 4x | Scanning lens
100x | = | 10x | 10x | Low power lens
400x | = | 10x | 40x | High power lens
1000x | = | 10x | 100x | Oil immersion lens

## Slide 11: The most important lens in microbiology is the oil immersion lens because it is provide the highest magnification and must be used with immersion oil . Immersion oil has the same refractive index as glass , so the oil becomes part from the optics of the microscope . By placing immersion oil between the glass slide and the oil immersion lens (100x) , the light rays at the highest magnification can be retained. Without placing the oil ,the light rays are refracted as they enter the air between the slide and lens , so ,the objective lens would have to be increased in diameter in order to capture them . Thus using oil has the same effect as increasing the objective diameter , therefore improving the resolving power of the lens.

## Slide 13: Microscope care Microscope is a very important tool in microbiology and it must be used carefully and correctly . Follow these guidelines every time you use a microscope : 1- carry the microscope with both hands , one hand beneath the base and the other on the arm . Never slide a microscope a cross a bench surface . 2- Clean the microscope both before and after use . Use only lens paper and lens cleaner . 3-Only use oil when using the 100X oil immersion lens . Do not get oil on the other objective lenses. 4-Do not wrap the cord around the microscope . Instead , fold the cord and place it between the arm and the stage or beneath the stage. 5- Observe the slide with both eyes open , to avoid eyestrain. 6- Always focus with low power first . 7- Keep the stage clean and free of oil . 8- wipe oil off the oil immersion lens before putting your microscope away . Do not touch the lenses with your hands . 9- Clean the ocular lens carefully with lens paper if dust is present . 10- Replace the dust cover before putting the microscope away . 11- Make sure that the specimen is on the top –side of the slide when using the oil immersion lens . 12- Increase the amount of light when using the oil immersion lens .