## Slide 1: Chapter One Elasticity

## Slide 2: Elastic Properties of Materials
Stress
Strain
- Young’s Modulus

## Slide 3: Stress and Strain
Stress is a quantity that is proportional to the force causing a deformation.
Stress is the external Force acting on an object per unit cross-sectional Area.
Strain is the result of stress ,which is the measure of the degree of deformation .

## Slide 4
Compression
Stress
Shear
Stress
Tension
Stress
Types of stress

## Slide 5: Types of Stress
Tension of Stress : is the force per unit area producing elongation of an object.
Tension
F
F

## Slide 6
Compression of Stress : is the force per unit area producing compression of an object.
F
F
Compression

## Slide 7
Shear of Stress : is the opposite “sliding force “ applied to parallel force of the object . Producing change in shape of material without changing its volume
Shear
F
F

## Slide 8
Stress
Stress : Force per unit area
=
F:Force applied in Newton
A:cross sectional area in m2
 : Stress in N/m2
A
F

## Slide 9: Strain :Ratio of elongation of material to the original length
 =, where : l : elongation(m),lo : original length of a material (m) and  is strain ,Dimensionless.
Elongation l =lf – lo
Where : lf loaded length of a material(m)
lf
lo

## Slide 10: Relation between Stress and Strain
The relation between the stress and the strain for a material under tension can be found experimentally .
A plot of stress vs. strain .
The diagram gives us the behavior of the material and material properties

## Slide 12: Elastic Limit
For small values of the strain , the stress – strain graph is a straight line ; the stress  is linearly proportional to the strain  .Beyond the linear limit A ,the stress is no longer linearly proportional to the strain .However ,from A to the elastic limit or yield point B ,the object still returns to its original dimensions when the applied force F is removed .

## Slide 13
The deformation up to B is said to be elastic
If the applied force is further increased ,the strain increased rapidly . In this region ,if the applied force is removed ,the object does not return completely to its original dimensions; it retains a permanent deformation .The highest point C on the stress-strain graph is the ultimate tension strength 1 of the material or its maximum stress .Beyond this point ,additional strain is produced even by a reduced applied force , and fracture occurs at point D .From B to D the material is said to undergo plastic deformation .If the ultimate tension strength and fracture points C and D are close together , the material is brittle ; if they are far apart the material is said to be ductile

## Slide 14
Young’s modulus of elasticity is a value that measures a materials resistance to being deformed elastically .
Hardness is a measure of how resistant solid matter is to various kinds of permanent shape change when a compressive force is applied .

## Slide 15: Young’s Modulus and Hook’s Law
In the linear region of the strain vs. stress diagram , the slope equals the stress-strain ratio and is called Young’s Modulus or Elastic Modulus (E) of the material .

## Slide 16
Stress(MN/m2)
strain
Breaking point
Elastic limit
Elastic behavior

## Slide 17
Elastic Modulus =
Y =
Example:
A 108N/m2 stress produces a strain 5x10-4.What is Young’s modulus for this bar?
Solution :
Y = = = 20x1010 N/m2

## Slide 18: Deformation types and define an elastic modulus
1.Young’s modulus ,which measures the resistance of a solid to a change in its length.
نتوقع معامل يونح للحديد اكبر من معامل يونج للمطاط
2. Shear modulus ,which measures the resistance to motion of the planes within a solid parallel to each other.
3. Bulk modulus , which measures the resistance of solider or liquids to changes in their volume.

## Slide 19: Young’s Modulus : Elasticity in Length
Y= = Young’s modulus
Young’s modulus is typically used to characterize
a rod stressed under either tension or compression .

## Slide 20: Shear Modulus :Elasticity of Shape
Y = = Shear modulus
Where
F
-F
h
Fixed face

## Slide 21: Bulk Modulus : Volume Elasticity
Y = = = - Bulk modulus
-A negative sign is inserted in this defining equation so that Y is a positive number . This maneuver necessary because an increase in pressure ( positive P) cause a decrease in volume ( negative V) and vice versa.
Vi
F
Vi+V

## Slide 22
substance | Young’s Modulus (N/m2) | Shear Modulus (N/m2) | Bulk Modulus (N/m2)
Tungsten | 35x1010 | 14x1010 | 20x1010
Steel | 20x1010 | 8.4x1010 | 6x1010
Copper | 11x1010 | 4.2x1010 | 14x1010
Brass | 9.1x1010 | 3.5x1010 | 6.1x1010
Aluminum | 7.0x1010 | 2.5x1010 | 7.0x1010
Glass | 6.5-7.8x1010 | 2.6-3.2x1010 | 5.0-5.5x1010
Quartz | 5.6x1010 | 2.6x1010 | 2.7x1010
Water | --------- | ------- | 0.21x1010
Mercury | --------- | ------- | 2.8x1010
Typical Values for Elastic Moduli

## Slide 23
Example :
How much pressure is needed to compress the volume of an iron block by 0.10 percent ? Express answer in N/m2 , and compare it to atmospheric pressure (1.0x105 N/m2) ?
Yong’s modulus for iron (90x1010 N/m2 )
Solution :
Y = -
=
Then : 90x1010 = -
P= 90x106 N/m2

## Slide 24: Hook’s Law
The linear stress – strain region in the diagram is called Hook’s Law region .In this region ,since the stress is linearly related to the strain . The force is linearly related to the elongation .

## Slide 25
F = - k x
Where”
K is force constant.
Y =
 = and
Then :
= Y
Thus , in tension or compression
the force on an object is proportional
to its elongation
Original x=0
New x=0
x

## Slide 26
Then :
F = k
Where k is the spring constant ,
ينطبق قانون هوك على المواد في المنطقة التغير الخطي بين الاجهادstress والانفعال strain.
وتكون قيمتة (K)كبيرة بزيادة مساحة المقطع بينما تقل بزيادة الطول

## Slide 27
Example:
A solid brass sphere is initially surrounded by air , and the air pressure exerted on it is 1x105N/m2 (normal atmospheric pressure ).
The sphere is lowered into the ocean to a depth where the pressure is 2x107N/m2 .The volume of the sphere in air is 0.5m3 .By how much does this volume change once the sphere is submerged ?

## Slide 28: Example :
A vertical steel girder with a cross-sectional area of 0.15m2 has a 1550 kg sign hanging from its end (Ignore the mass of the girder itself .)
( a ) what is the stress within the girder?
( b ) What is the strain on the girder ?
( c ) If the girder is 9.50 m long , how much is it lengthened ?

## Slide 29
Example :
A 15 cm long tendon was found to stretch 3.7 mm by a force of 13.4 N . The tendon was approximately round with an average diameter of 8.5 mm .Calculate the elastic modulus of this tendon .

## Slide 30
Example :
A nylon tennis string on a racquet is under a tension of 250N . If its diameter is 1.00 mm , by how much is it lengthened from its un – tensioned length ?

## Slide 31
Example
A bar has dimensions 1 cm by 1cm by 20cm .It is subjected to a 10000N tension force and stretches 0.01cm . Find :
( a ) the stress;
( b ) the strain;
( c ) If the stress-strain graph is straight line ,how much does the bar stretch when the applied force is increased to 50000N?

## Slide 32: Poisson’s ratio Shear stress – strain diagram
L
P
P
d
L’
d’

## Slide 33
Definition
When a deformable body is stretched by a tensile force ,not only it does elongate but it also contract laterally . i.e. it would contract in other two dimensions.
Likewise , a compressive force acting on a deformable body cause it to contract in the direction of force and yet its sides expand laterally .
When the load P is applied to the bar it changes the bar’s length by  and its radius by r .The strain in axial direction and in lateral / radial direction are respectively .

## Slide 34
In early 1800s, French scientist Poisson realized that within elastic range the ratio of these two strains is a constant . We called the constant as Poisson’s ratio by

## Slide 35
long =
lat =
Then the Poisson’s ratio define as :
Poisson’s ratio == -
 = -
In tension the long is ( + ) and lat is ( - )
But in compression state the long is ( - ) and lat is ( + )
The value of 0

## Slide 36
Poisson’s ratio for important material
Material | Poisson’s Ratio
Cork | 0.5
Rubber | 0.48 to 0.5
Lead | 0.44
Copper | 0.37
Aluminum | 0.35
Stainless Steel | 0.3
Steel | 0.29

## Slide 37
Remarks:
The lateral strain is caused only by axial force .No force or stress acts in lateral direction ,
Lateral strain is the same in all lateral direction
Usually 0
elastic material =0.3.
.Poisson’s ratio is a constant

## Slide 38
Question :
For a 10 m rod made of the material with Poisson’s ratio =0.3,that has elongated by 12mm ,what is its new radius if originally it had a radius of 50mm?
(a)50.018mm (b)49.982mm (c ) 50.400mm (d)49.600mm

## Slide 39: Shear Stress-strain relation
Stress()
Strain()
Proportional
limit
Ultimate stress
Fallure stress
Modulus of rigidity , G
(or shear modulus of elasticity
=G
=E

## Slide 40: Material property relations
G=E/(2(1+))
Where: E is Young’s modulus
G is modulus of rigidity
 is Poisson’s ratio

## Slide 41
Example:
A cubic block with each side of original length 4 in . Is subjected to the compressive force as shown . If its sides along the x and y direction increased to 4.0001 in , determine  and G for the material .Assume it behaves elastically and E=10x103 ksi
4in
10 kip