## Slide 1
Lec 3 5th stage
Advanced Pharmaceutical Chemistry
2018-2019
Assist prof. Dr.Rita Sabah Elias
College of Pharmacy, university of Basrah

## Slide 2
Boltzmann distribution in NMR-effect of field strength and temperature
In B0 the nuclei divide themselves between two energy levels(spin 1/2 nuclei. The relative numbers of nuclei occupying each level (once thermal equilibrium has been achieved) can be calculated according to Boltzmann distribution law.
It is clear that, for net absorption to occur there must be more particles in the lower energy state than in the higher energy state. So we can calculate from the Boltzmann law the relative number occupy each level. The boltzmann law is

## Slide 3
Example:- At 25 °C what fraction of 1H nuclei in 5.87T field are in the upper and lower states?
,

## Slide 4
every million nuclei in the higher energy state (for protons at25°C in a 5.87 T magnet) there is an excess of only 20 in the lower energy state (an excess of 20 ppm). And difference for other elements is even smaller because of their smaller γ valleue.
If the populations of the upper and lower states become exactly equal, we observe no net signal. This situation is called saturation. Therefore, the very small excess of nuclei in the lower spin state is quite important to NMR spectroscopy, and we can see that very sensitive NMR instrumentation is required to detect the signal. If we increase the operating frequency of the NMR instrument, the energy difference between the two states increases, which causes an increase in this excess. Following table shows how the excess increases with operating frequency.

## Slide 5
Operating frequency (MHz) | 1H Excess nuclei
20 | 3
40 | 6
60 | 9
80 | 12
100 | 16
200 | 32
300 | 48
600 | 96
It also clearly shows why modern instrumentation has been designed with increasingly higher operating frequencies. The sensitivity of the instrument is increased, and the resonance signals are stronger, because more nuclei can undergo transition at higher frequency. Before the advent of higher-field instruments, it was very difficult to observe less-sensitive nuclei such as carbon-13, which is not very abundant (1.1%) and has a detection frequency much lower than that of hydrogen.
Variation of 1H Excess nuclei with operating frequency

## Slide 6
Number of signals
The number of signals in the NMR tells the number of different sets of equivalent protons in a molecule. Each signal corresponds to a set of equivalent protons. It may be noted that magnetically equivalent protons are chemically equivalent proton.
Chemically equivalent protons: - are protons in identical electronic environments, and have the same value of chemical shift in NMR spectroscopy.
Chemical equivalent→ chemical shift equivalent
Magnetically equivalent→ coupling equivalent

## Slide 7
Compounds showing one signal

## Slide 8
Compounds showing more than one signal
Compounds showing more than one signal, a molecule that has sets of protons that are chemically distinct from one another may give rise to a different absorption peak from each set, in which case the sets of protons are chemically nonequivalent

## Slide 9
Chemically equivalent protons must also be stereo chemically equivalent, particular set of protons are said to be chemically equivalent only if they remain in exactly similar environment when the stereo-chemical formula of the molecule under consideration is written

## Slide 10
Positions of signals (Chemical shift)
The number of signals in the NMR → the number of sets of equivalent protons in a molecule

## Slide 11
It is important to note that it is electronic environment which tells where a proton shows absorption in the spectrum.